## Slide 1: A Softcore RISC-V Vector Processor for Edge AI
V Naveen Chander
MTech Dissertation Project
Microelectronics and VLSI Design,
Supervisor: Kuruvilla Varghese
Dept. of Electronic Systems Engineering,
Indian Institute of Science
23rd June 2021

## Slide 2: Objective Enabling Scalable and efficient ML inference at the edge
Develop microarchitecture for microcontroller class CPU to significantly speed up ML inference

## Slide 3: Motivation
Edge computation is gaining ground with the advent of AI-IoT
Deep Neural networks are growing wider and deeper in size
  Becoming increasingly difficult to deploy on conventional micro-controller-based systems
  Painful trade-offs to be carried out between power, latency and accuracy.
Profiling analysis of ML inference workloads reveals that more than 99% time the CPU is busy executing matrix/vector operations
  Strong need for Data-level parallelism for efficient ML inference.
  Require domain-specific ISA with strong descriptive capacity for Neural Networks and support general purpose computing
RISC-V Vector (RVV) Extension defines an ISA for dealing with vectors
  A vector execution unit tightly-coupled with the scalar RISC-V core can be used to enable efficient ML inference.

## Slide 4: Workflow
ML Bottleneck Analysis
Identify commonly used ML inference algorithms
Microarchitecture Design
Develop a modular Vector Unit to execute Vector Instructions from RISC-V Vector ISA
Evaluation and Demonstration
Develop vectorization algorithms for neural network layers
Develop C programs for Neural Networks
Run and profile Neural Networks to identify portions of code where CPU spends the maximum time
Interface the Vector Unit with a microcontroller class RISC-V host processor
Run programs on Scalar and Vector RISC-V CPUs
Compare performance of Vector core with scalar core and other data-parallel microcontroller cores
Implement design on Xilinx Vertex-7 FPGA
Demonstrate Image Classification task on the vector processor

## Slide 5: Computational Bottlenecks in ML
C-code profiling was carried out for MLP, CNN, PCA, AE, RNN, LSTM on x86 and ARM targets
Findings :-
  Many NN topologies have some common operations such as -
    Matrix Vector Multiplication in MLP, CNN, RBM, AE, PCA, RNN, LSTM
    Matrix Convolution  Vector Dot Product in all CNNs, Capsule Networks
    Vector Multiplication with Scalar
    Exponent Computation of elements in a vector
  In all NNs, >99% time, CPU is busy with Matrix/Vector operations
KEY TAKEAWAY
Need to exploit the data-level parallelism in ML inference
Effect of SIMD on performance of Matrix Vector Multiplication
Distribution of Execution Time on CNN (left) and RNN(right)
Effect of SIMD on Execution Time on Intel i386 CPU for a 6-layer CNN
Without SIMD
With SIMD
4.1x
3.1x
3.1x
5.8x
3.5x
14.5x

## Slide 6: Related Work
Topology | Pros and Cons
Hardware ML Accelerators | Fastest and Most energy-efficient; but lack support for Gen. purpose ISA
Multi-core and Many core CPUs | Good speedup, poor energy efficiency as they fail to exploit Data Level Parallelism in ML
Data-parallel CPUs such as SIMD and Vector | Exploit DLP. Can achieve significant speedups with minimal energy overheads
VEGAS
2009, Soft Vector Processor IP
FPGA based Softcore Vector Processor targeted at Image Processing Applications
Operates at 100 MHz and Features a scratchpad Memory and a decoupled Vector Unit
Klessydra-T
2021, Vector Processor for Edge-AI
3 cores, 105 MHz with vector Unit with Scratchpad Memory on FPGA
Although Host CPUs are RISC-V Cores, Vector Unit does not use RVV
PULP CE32V40
2017, Low-power Data-parallel SIMD CPU
OpenRISC Core ASIC with DSP extensions
Use SIMD unit with custom instructions to handle vectors
Targeted at 8-bit, 16-bit computations
Ongoing project on RISC-V Vector CPU for Edge-AI
British Computer Society Open Source Specialists
Studied Workload of ML-inference and arrived at the similar conclusions
Use RISC-V Vector Unit with PULP CE32V40
Demonstrated speed-ups at the level of Functional Simulation on FPGA (12th February, 2021)

## Slide 7: RISC-V Vector Extension ISA Specification
RVV-ISA is a document that defines the ISA for RISC-V vector extension
ISA is yet to be ratified. The current Vector Processor design adheres to spec. Ver 1.0
Features
  RISC-V ISA is open and free for use
  No licensing requirements
  RISC-V ISA is modular
  RISC-V Vector (RVV) Extension is exhaustive
  RVV allows users to choose subsets of the extension to be implemented
  Allows usage of General purpose and Vector Instructions together
RVV Overview
  Organization of Data in Vector Registers
  Instructions for Vector Loads and Stores
  Instructions for Vector Arithmetic Operations  300 + instructions
  Vector Reduction Instructions
  Vector Permutation Instructions
This work uses 53 vector instructions to accelerate ML inference

## Slide 8: Specifications of the RISC-V Vector CPU
Parameter | Specification
CPU | Single-core, single-issue, in-order, 5-stage pipeline
Operating Frequency | 50 MHz
Memory | I-Cache : 8KB , 2-way Set Associative D-Cache : 8KB, 2-way Set Associative Main Memory : 1MB
ISA Support | RV32gV
Peripheral | UART (1 port)
Vector Accelerator | 8-lane Integer Vector Unit Vector Memory: 128kB Scratchpad memory
Power Consumption | 597 mW
XILINX VERTEX-7
XC7VX485TFFG1761-2
FPGA
featuring
RISC-V Vector CPU
Soft-IP
CLK
RST
CTS
UART_RX
RTS
UART_TX

## Slide 9: Microarchitecture
Vector Execution Model and Theoretical performance
Vector Execution Unit microarchitecture and results
Integration of Vector Unit to Host CPU

## Slide 10: Vector Execution Model
vle32.v v4, t1
F
D
E
M0
M1
M2
…
M31
W31
F
D
E0
E1
E2
…
E31
Total Vector Execution Time = 44 Cycles; Chime Estimate=32 cycles; Overheads = 12 cycles
R
CONVOY
R
Vector Arithmetic Units operate on Vectors that are stored in a Vector Register File.
Assume we have a 6-stage pipeline: Fetch Decode Read Execute Memory-> Write back
Assume, we have an 8-lane Vector Processor
F
D
E
M0
M1
M2
…
M31
W31
R
M31
W31
F
D
E
M0
M1
M2
…
M31
W31
R
F
D
E
M0
M1
M2
…
M31
W31
R
F
D
E0
E1
E2
…
E31
R
M31
W31
F
D
E0
E1
E2
…
E31
R
M31
W31
F
D
E0
E1
E2
…
E31
R
M31
W31
vle32.v v8, t2
vle32.v v8, t2
vle32.v v8, t2
vmacc.vx v20, s0, v4
vmacc.vx v20, s1, v8
vmacc.vx v20, s2, v12
vmacc.vx v20, s3, v16
Lane1
Lane2
Lane3
Lane4
Lane5
Lane6
Lane7
Lane8

## Slide 11: Analytical measurement of Performance on VMATMUL32
Scalar Core
  Assume an ideal scalar processor that has CPI=1
  All Cache-hits and no hazards in pipeline
  Runs a fully optimized assembly code for VMATMUL
Vector Core
  Can operate up to eight elements per cycle
  Takes 44 cycles to execute 32 elements
  Vectorization results in 8 convoys
  Scalar instructions run at CPI = 1
Parameter | Scalar Core | Vector Core
No. of Static Instructions | 17 | 22
No. of dynamic Instructions | 7626 | 145
Cycles to execute | 7630 | 520
Ideal Speedup | 1 | 17.6
Deviations from Ideal Condition that contribute to variation in Speedup
I-Cache, D-Cache Miss Penalties
Hazard Penalties
Handshaking cycles(only for Vector Proc)

## Slide 12: Design of RISCV-Vector Execution Unit
Systolic Array based Vector Execution
  Network of eight identical processing elements
  Use shared resources such as Register files and memory
  Execution of P.Es is tightly coupled => P.E != HART
Novel Architecture with
  Systolic Array execution unit
  Scratchpad memory based Vector Memory Unit

## Slide 13
VRF
Bank 0
32 x 32
Elements
0, 8, 16, 24, …
P.E
DMEM Bank 0
X- BAR
P.E
DMEM Bank 1
P.E
DMEM Bank 2
P.E
DMEM Bank 3
P.E
DMEM Bank 4
P.E
DMEM Bank 5
P.E
DMEM Bank 6
P.E
DMEM Bank 7
RA
RB
W
VRF
Bank 1
32 x 32
Elements
1, 9, 17, 25, …
RA
RB
W
VRF
Bank 2
32 x 32
Elements
2, 10, 18, 26, …
RA
RB
W
VRF
Bank 3
32 x 32
Elements
3, 11, 19, 27, …
RA
RB
W
VRF
Bank 4
32 x 32
Elements
4, 12, 20, 28, …
RA
RB
W
VRF
Bank 1
32 x 32
Elements
5, 13, 21, 29, …
RA
RB
W
VRF
Bank 2
32 x 32
Elements
6, 14, 22, 30, …
RA
RB
W
VRF
Bank 3
32 x 32
Elements
7, 15, 23, 31, …
RA
RB
W
Lane 1
Lane 2
Lane 3
Lane 4
Lane 5
Lane 6
Lane 7
Lane 8
WB_FIN
MEM_WB
EXE_MEM
RD_EXE
BLOCK SCHEMATIC OF PIPELINED VECTOR EXECUTION UNIT

## Slide 14
I-MEM
ADDR
DOUT
PC
REG
CLK
CLK_EN
D
REG_FILE
R0-R31
DT1
DT2
RD#1
RD#2
WR#
RWR
DATA_IN
IMM32
GEN
00
11
01
10
00
11
01
10
BLU
00
11
01
10
00
11
01
10
ALU
CONTROL
D-MEM
ADDR
DOUT
DIN
dmr
dmw
1
0
I(19:15)
I(24:20)
RS1+IMM32
rd
+
00
11
01
10
PC + IMM32
PC+4
PC
1
0
NOP
I(31:0)
c_hazard
11
01
00
10
00
01
01
10
1
0
ALUop
+
+
IF/ID.PC + IMM32 - 4
<<1
RS1_FWD + IMM32
D_FB
D_FA
E_FB
ZERO
ZERO
M_FB
ZERO
FOUR
IF/ID
ID/EX
EX/MEM
MEM/WB
WB/FIN
rwr
ALUSrc
memreg
Block Schematic of Scalar RISC-V Pipeline

## Slide 15
V-MASK UNIT 7
V-MASK UNIT 7
V-MASK UNIT 7
ALU 7
32 bit
ALU 7
32 bit
ALU 7
32 bit
D-MEM
Bank 7
1k x 32
ADDR
DOUT
DIN
dmr
dmw
D-MEM
Bank 7
1k x 32
ADDR
DOUT
DIN
dmr
dmw
D-MEM
Bank 7
1k x 32
ADDR
DOUT
DIN
dmr
dmw
VRF
BANK 7
v0-v31
32-bit
DT1
DT2
RD#1
RD#2
WR#
RWR
DATA_IN
MASK
VRF
BANK 7
v0-v31
32-bit
DT1
DT2
RD#1
RD#2
WR#
RWR
DATA_IN
MASK
VRF
BANK 7
v0-v31
32-bit
DT1
DT2
RD#1
RD#2
WR#
RWR
DATA_IN
MASK
ID/RD
VRF
BANK 7
v0-v31
32-bit
DT1
DT2
RD#1
RD#2
WR#
RWR
DATA_IN
MASK
DT3
DT4
ALU 7
32 bit
D-MEM
Bank 7
4k x 32
ADDR
DOUT
DIN
dmr
dmw
V-MASK UNIT 7
.
.
.
.
.
.
1
0
1
0
1
0
1
0
.
.
.
.
.
.
RD/EXE
EXE/MEM
MEM/WB
ALU 7
32 bit
ALU 7
32 bit
ALU 7
32 bit
LSU 7
32 bit
STALLER
SYSTOLIC
ARRAY
SEQUENCER
CHAINING
CHAINING
DT3_Xbar
DT2_Xbar
DT1_Xbar
Vector Interface Unit
Instruction – 07
WB/FIN
x1
x2
x3
x4
DT4_Xbar
FROM SCALAR TO VECTOR PIPELINE

## Slide 16: Systolic Array Sequencer
Functions
  Distributes Instructions to Vector Lanes
  Schedules Execution
  Distributes Shared Resources
Design
  Hierarchical Sequencer
  Each Vector Lane has a micro sequencer
  The top level sequencer coordinates execution of all eight micro sequencers

## Slide 17
SYSTOLIC ARRAY SEQUENCER –LANE SEQUENCER
VRF
Bank 0
32 x 32
Elements
0, 8, 16, 24, …
P.E
DMEM Bank 0
X- BAR X1
DMEM Bank 1
DMEM Bank 2
DMEM Bank 3
DMEM Bank 4
DMEM Bank 5
DMEM Bank 6
DMEM Bank 7
RA
RB
W
VRF
Bank 1
32 x 32
Elements
1, 9, 17, 25, …
RA
RB
W
VRF
Bank 2
32 x 32
Elements
2, 10, 18, 26, …
RA
RB
W
VRF
Bank 3
32 x 32
Elements
3, 11, 19, 27, …
RA
RB
W
VRF
Bank 4
32 x 32
Elements
4, 12, 20, 28, …
RA
RB
W
VRF
Bank 1
32 x 32
Elements
5, 13, 21, 29, …
RA
RB
W
VRF
Bank 2
32 x 32
Elements
6, 14, 22, 30, …
RA
RB
W
VRF
Bank 3
32 x 32
Elements
7, 15, 23, 31, …
RA
RB
W
Lane 1
Lane 2
Lane 6
Lane 7
Lane 8
X- BAR X2
X- BAR X3
Lane 3
Lane 4
Lane 5

## Slide 18: Vector Memory
Scratchpad memory based on SRAM
Capacity 128 kB (4k x 4 x 8)
Latency of 1 clock cycle
Organized as 8 banks
SPRAM
Bank 0
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 1
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 2
16KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 3
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 4
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 5
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 6
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
SPRAM
Bank 7
16 KB
0
1
2
4095
ADDR[11:0]
DIN[31:0]
DOUT[31:0]
WE
Controlled by programmer
Mainly used for storing vectors
Shown to provide 1.2x – 3x performance improvement over cache

## Slide 19: Implementation Results of Standalone Vector Unit
Power Distribution
Total Power : 120 mW
LUT Distribution
Registers Distribution

## Slide 20: Integration of Vector Unit
HOST CPU
Host CPU
  Microcontroller class softcore with 1MB RAM and UART peripheral
  Single core, 5-stage, single-issue, in-order CPU
PIPELINED VECTOR UNIT
…
iBuf0
iBuf1
iBuf2
iBuf7
Vector Read Stage R
Vector Execute Stage E
Vector Memory Stage M
Vector Write-back Stage W
DONE
DECODED_OPRNDS,CTRL
118
STALL
Scratchpad Memory
and
Vector
Register
Interface
Lane1
Lane2
Lane3
Lane8
Vector Interface Unit (VIU)
32
66
ADDR, DATA_WR, RD,WR
32
DATA_RD
xREG_DATA
64
H-SHAKE
PC_CTRL
INSTRUCTION
V_BUSY
START
Interface
  Tightly Coupled Integration  Vector Unit is attached onto the Host CPU’s pipeline
  Uses Native Bus Interface for low latency communication
  Vector and Scalar execute in a mutually exclusive manner using handshake signals
  VIU directly receives the instruction read from the Memory for decoding
  Additionally the host CPU has access to Vector Register File and Vector Memory
Parameter | Specification
CPU | Single-core, single-issue, in-order, 5-stage pipeline
Operating Frequency | 50 MHz
Memory | I-Cache : 8KB , 2-way Set Associative D-Cache : 8KB, 2-way Set Associative Main Memory : 1MB

## Slide 21: VIU Sequencer
S1
S2
V2
V3
V4
V5
V6
V1
V7
V8
S3
S4
S
V
S
V
V
V
V
V
V
V
V
V
V
V
V
V
V
V
S
S
S
S
S
S
S
S
S
S
S
S
S
S
S5
S6
S7
S8
INSTRUCTION
SCALAR PIPELINE
VECTOR PIPELINE

## Slide 22: Top Level Design
FPGA Device die view post Implementation on Xilinx Vertex-7 xc7vx485tffg1761-2 FPGA
Overall Resource Utilization ~ 26%
Resource Utilization
Power Consumption
On-chip Power | Static | Dynamic | Total
Vector CPU | 264 mW | 333 mW | 597 mW
Scalar CPU | 263 mW | 233 mW | 496 mW
Vectored Power Estimation using Xilinx Power Analyser by running CNN on CPUs in Post-layout Simulations
Timing Analysis
Power Estimation

## Slide 23: Evaluation
Benchmarking
Demonstration on Image Recognition task

## Slide 24: Evaluation Plan
Criteria
  Performance
  Power
Benchmarking
  Custom suite of programs devised
  Based on identified computational workloads
  30 programs under 6 classes
Vector Programming
  Devised Vectorization Algorithms for benchmark kernels
  Enable programmer write codes that make efficient use of hardware.
  RVV Assembly with C-wrapper function
Evaluation Metrics
  Average cycle count per algorithmic operation
  Maximum Clock Frequency
  Absolute Execution Time
  Average Energy per algorithmic operation
Comparison
  Scalar vs Vector: All benchmark programs run on Scalar and vector Cores
  RISCV-V Vector vs. other Data parallel machines:
    Klessydra-T (softcore)
      Vector Processor with 3 HARTS
      105 MHz with Vector Unit and Scratchpad Memory
      Targeted at Edge-AI (2021)
    CE32V40 (ASIC)
      Ultra-low power SIMD processor by PULP Platform
      91.4 MHz
      Targeted at data-parallel computations (2017)

## Slide 25: Benchmarking Results
RISC-V Vector vs Scalar Comparison on AXPY, Perceptron, MATMUL and CONV
  AXPY is least computationally intensive and requires least memory.
  MATMUL requires highest memory.
  CONVOLUTION has the highest arithmetic intensity.
  Scalar Code compiled with gcc –O3
Performance
  Vector CPU has a speedup between 2.5x and 63x
  Speedup can be mainly attributed to vector acceleration and use of Scratchpad memory
  AXPY and CONV achieve near-theoretical speedup of 17x
  MATMUL and Perceptron achieve speedups more than the ideal speedup due to memory bottleneck in the scalar core.
  Speedup variation is not smooth over vector lengths due to non-linear increase in execution time on scalar core due to
    Different ways of optimization used by the compiler
    I-Cache and D-Cache Cache misses
Energy per Algorithmic Operation
  Calculated by
  Even though the scalar CPU consumes 100 mW lesser, spends more energy due to increased execution time.

## Slide 26: Speedup variation with Vector length
Speedup increases with vector length before it begins to saturate
Low speedup for small vectors can be attributed to
  High vector unit overheads
  Better compiler optimization for scalar code
  Reduced probability of cache miss
Accounting for speedup
  About 17x is the theoretical speed-up
  Due to increased number of instructions and data fetched by the scalar core, it loses many cycles in miss penalties (miss penalty=23 cycles)
  About 1.3x -2.5x speedup is contributed by using Scratchpad Memory

## Slide 27: Comparison with Other Data-parallel Processors
RISC-V Vector CPU performs comparably with Klessydra Vector Processor
RISC-V Vector CPU performs better than SIMD processor on Convolution, but SIMD has an edge over Vector processor on MATMUL64

## Slide 28: Performance on Neural Networks
Multi layer Perceptron
Convolutional Neural network
SPEEDUP: 40.7x
SPEEDUP: 19.53x
ENERGY IMPROVEMENT: ~ 33x
ENERGY IMPROVEMENT ~ 16x

## Slide 29: Summary and Future Work
Main Contributions
  Bottleneck analysis of ML Inference
  A microarchitecture for efficient ML inference on microcontroller class CPUs
  Tightly coupled Vector Execution Unit
  Benchmark targeted at ML workloads
  Vectorization Algorithms for kernels commonly encountered in ML inference
Future Work
Support for low precision vector arithmetic
  8-bit/16-bit numbers multiply performance without much loss in accuracy
DMA for Scratchpad memory
  Avoid CPU time to be wasted in copying data from amin memory to scratchpad memory
Increased Clock Frequency of operation
  Make changes in the host such as remove FPU, change Cache-replacement algorithm to increase operating frequency above 50 MHz
Mixed Signal Accelerators
  The developed Vector Interface is robust, and the vector unit is modular.
  The present vector unit can be replaced with an Analog Accelerator designed in the future

## Slide 30: Demonstration: Handwritten Digit Recognition by Vector Processor
Demo Video /Demo Action

## Slide 31: THANK YOU