## Slide 1: CV32E40P Interrupt Vplan Review
Steve Richmond steve.richmond@silabs.com
September 29, 2020

## Slide 2: Outline
Assumptions
Test overview
CSR exceptions
Vplan issues – External Excel sheet

## Slide 3: Assumptions
ISS runs for all tests
  Step and compare logic deasserts deferint to ISS 1 retirement away from the irq_ack_o signal
Interrupt assertion module implemented from the vplan is enabled for all tests

## Slide 4: Test Overview
Directed tests
  interrupt_test – Set of directed tests (developed in C) to verify basic interrupt functionality
    Developed as a set of subtests
      1. Iterate through all 32 interrupt sources to ensure no reserved interrupts taken and enable combinations (MIE, MSTATUS.MIE) work properly
      2. Trigger all IRQs at once and ensure that the interrupts are handled in priority order
      3. Basic nested interrupts – somewhat random, ensure that an interrupt can be taken after stacking mie, mstatus and mepc and be handled properly (Follows RM algorithm)
      4. WFI – Only MIE-enabled interrupts may WFI. Tests that WFI wake occurs regardless of MSTATUS.MIE (but IRQ handler not taken if MSTATUS.MIE == 0)
      5. Relocates the vector table (tests write of MTVEC) and iterates through all interrupts as a repeat of test 1
      6. Relocates the vector table to a DIRECT mode and iterates through all interrupts as a repeat of test 1
      7. Repeat test 1 in vectored mode relocated to the default vector table

## Slide 5: Test Overview
Directed tests
  interrupt_bootstrap
    Uses plusarg to set initial mtvec pins value (bootstrapped upon initial core fetch) to alt table
    Uses test1 from interrupt_test to iterate through interrupts
    Tests that mtvec is read properly with bootstrap value

## Slide 6: Test Overview
Random tests
  corev_rand_interrupt
    Randomly asserts interrupts via uvma_interrupt
      3 random sequences in virtual sequence
        Assert and deassert via irq_ack_o (may randomly hold through a single irq_ack_o)
        Assert arbitrary irqs
        Deassert arbitrary irqs
      May assert interrupts immediately out of reset during core initial fetch
    corev-dv – extensions
      corev_interrupt_csr_instr_stream – randomly inserts MSTATUS.MIE flips and MIE writes during testing
      enable_fast_interrupt_handler – the standard ISR inserted by riscv-dv fully stacks and unstacks the GPRs with some other CSR reads (for ISS checking). This extension will randomly replace all of that code with a single “mret”

## Slide 7: Test Overview
Random tests
  corev_rand_interrupt_wfi
    All testing from corev_rand_interrupt in addition to the following:
    +no_wfi = 0 – WFI instructions are randomly inserted by riscv-dv into the random instruction stream
    The CSR sequence will never set MIE to 0 (infinite stall with WFI)

## Slide 8: Test Overview
Random tests
  corev_rand_interrupt_nested
    All testing from corev_rand_interrupt_wfi
    Adds +enable_nested_interrupt
      Corev-dv extension to randomly add mstatus, mscratch, mie and mepc stacking to the mmode_intr_handlers to enable nested interrupts

## Slide 9: CSR Exceptions
The following interrupt-related CSRs have exceptions in CSR checking against the ISS (in uvmt_cv32_step_compare.sv)
  mepc – skipped for instruction retirement pre-cycle (i.e. same cycle as irq_ack_o) – checked in all other cycles
  mcause - skipped for instruction retirement pre-cycle (i.e. same cycle as irq_ack_o) – checked in all other cycles
  mstatus - - skipped for instruction retirement pre-cycle (i.e. same cycle as irq_ack_o) – checked in all other cycles
  mip – Never checked in ISS – checked in directed tests
    Primary complication is the auto-clear, I have to maintain mip signaling to the ISS when deferint is asserted, long after irq_i may have auto-cleared